# Text boxes

4 – QUADCONs Coupled Together

YA0314-01

L = 239”     W = 96”     H = 82”                Empty Weight = 5292 lbs

Payload Weight = 28308 lbs

Gross Weight = 33600 lbs

3 – TRICONs Coupled Together

YA0697-01 Green

YA0697-03  Tan

L = 239”     W = 96”     H = 96”                Empty Weight = 7800 lbs

Payload Weight = 36900 lbs

Gross Weight = 44700 lbs

ISU-90 = YA0175-01

ISU-60 = YA0166-01

1 – TRICON = YA0524-01

L = 96”     W = 78”     H = 96”

Empty Weight = 2600 lbs

Payload Weight = 12300 lbs

Gross Weight = 14900 lbs

1 - Quadcon = YA0313-01

L = 58”     W = 96”     H = 82”

Empty Weight = 1764 lbs

Payload Weight = 9436 lbs

Gross Weight = 11200lbs

20 ft MILVAN =YA0158-01 C13825 has several index numbers to chose from

463L Short Pallet

YA0159-01

L = 88”     W = 108”     H = 3”

Weight = 350 lbs

C130, C 141, C17 , C5, KC135

463L Long Pallet

YA0081-01

L = 108”    W = 88”    H = 3”

Weight = 350 lbs

KC10, C17 C3